## Slide 1: Hitcon Badge 2018
MEDIATEK 黃偉峻 MEDIATEK 李倫銓

## Slide 2: Guidline
Hardware overview
Subsystems
ETH Transaction
HD Wallet - BIP32,39,44
Secure Element with Wallet
Manufacture
Documents

## Slide 3: Hitcon Badge 2018

## Slide 4
MT7697 WiFi/BLE Soc
SLE97
2.13” e-Paper
Button Array
CP2102N
USB to UART
3V to 3.3V
Step-up
5V to 3.3V
LDO
PN532
NFC controller
SPI bus
I2C bus
Interrupt
Analog
UART
USB
5V
3.3V
3.3V
Special buttons
Digital
Hardware Diagram

## Slide 5: MT7697
192 MHz Cortex-M4F
WiFi 802.11b/g/n & BLE SoC
352KB Ram / External SPI flash
64KB Bootloader Rom
UART/SPI/I2C
Crypto-engine

## Slide 6: Linkit 7697
Arduino Support
Wrtnode’s module with 4MB Flash
MTK Official Support Platform
With Auto-Switch to load Firmware
Arduino IDE Setup:
https://docs.labs.mediatek.com/resource/linkit7697-arduino/en/environment-setup/setup-arduino-ide

## Slide 7: Hitcon Badge‘s Arduino Package
官方的版本有幾個狀況需要修改，所以直接Fork一版出來
Package:https://raw.githubusercontent.com/will127534/HITCON-Badge-2018/master/Software/Arduino_packages/package_hitcon_badge_index.json
修正改的內容:
  1.RTOS Tickless Sleep 移除了，多虧Android的Active Scanning
  2.BLE MTU Size
  3.Analog Read和Sleep的Bug
  4.關閉Wifi
  5.加入Secure Element+電子紙的Library

## Slide 8: Waveshare 2.13” Black and White e-paper
GDE0213B1 - Support Partial Update – takes only 0.2s

## Slide 9: PN532 – NFC controller
Not used, 時間來不及
天線形狀比較特殊，電路需要調整阻抗匹配
NFC 天線!

## Slide 10
Simulated
Real

## Slide 11: PN532 – NFC controller

## Slide 12: Button Array
MT7697沒有多的Digital pin了QQ
Solution: Analog Button Array
3.3V
Output

## Slide 13: Button Array
MT7697沒有多的Digital pin了QQ
Solution: Analog Button Array
3.3V
Output
13.4K 歐姆

## Slide 14: Button Array
MT7697沒有多的Digital pin了QQ
Solution: Analog Button Array
3.3V
Output
11.4K 歐姆

## Slide 15: Button Array
MT7697沒有多的Digital pin了QQ
Solution: Analog Button Array
3.3V
Output
9.4K 歐姆

## Slide 16: Button Array
需要精確的電壓和電阻
但是Badge上面有兩個供電，電壓升壓和USB降壓
透過使用者一定會按到的按鈕自動校正電壓
  Button ENTER + Button 6, 這兩個按下去之後會校正輸入的電壓

## Slide 17: Misc.
多數Interface都是以1K或者0歐姆電阻串接，方便斷開

## Slide 18: Misc.
正面的Power LED燈預設斷路以減少耗電量
USB 轉 UART 和其他供電有做隔離，避免CP2102N消耗電池
Battery有做防反接的保護

## Slide 19: Secure Element
SLE97 – From Infineon, Software from IKV
ARM® SecurCore™ SC300™
Crypto processor
ISO 7816 interface
SPI interface
CC EAL5+ high !

## Slide 20: Hitcon Badge 2018 Hardware overview
NFC 天線
電子紙
Button Array
Battery Switch
NFC
EPD
MT7697
Module
Secure
Element

## Slide 21: Wallet – Cryptocurrency
Hash
Sign
Transaction Data
Transaction Hash
Transaction Signature

## Slide 22: Wallet – Cryptocurrency: BTC
對比特幣來說，每一筆交易完成後，餘額會匯到新的錢包
錢包需要管理一堆Private Key
Private Key 管理問題
Solution: Deterministic Wallet
50 BTC
10 BTC
40 BTC
交易
A
A
B

## Slide 23: HD Wallet – BIP32,39,44 Overview
Root Seed
Mnemonic Code
HMAC-SHA512
Right 256bit
Master Chain Code
Left 256bit
Private Key m
Child Key m/0
Child ID
Child Chain code
…….
Child Key m/2
Child ID
Child Chain code
Child Key m/1
Child ID
Child Chain code
Grandchildren Keys m/0/0~2^32
Grandchildren Keys m/1/0~2^32
Grandchildren Keys m/2/0~2^32
BIP39
BIP32
BIP44
…….

## Slide 24: Child key derivation
Parent
Private or Public Key
HMAC-SHA512
Left 256bits
Right
256bits
Parent
Chain Code
index number
Child Private Key
Child Chain Code
Key
Data
https://github.com/bitcoin/bips/blob/master/bip-0032.mediawiki
Hardened
Notes: Hardened  避免 parent public key +Child Private Key 外洩造成 Parent Private Key 被讀出來

## Slide 25: BIP39 - Mnemonic Code
由於Root Seed 不方便人類抄寫，所以透過2048個字的組合定義一個Coding 方式
2048個字 每個字代表11byte
Word List:
Abandon 0x01
Ability 0x02
Able 0x03
About 0x04
.
.
.
https://github.com/bitcoin/bips/blob/master/bip-0039.mediawiki
Root Seed (128~256bit multiple of 32bit)
…….
11bit
11bit
11bit
11bit
…….
Mnemonic Words
First Seed Length/32 bit of SHA256(Root Seed)

## Slide 26: BIP39 - Mnemonic Code
https://github.com/bitcoin/bips/blob/master/bip-0039.mediawiki
Root Seed Length | Checksum Length | Total Length | Word Length
128 Bits | 4 Bits | 132 Bits | 12 Words
160 Bits | 5 Bits | 165 Bits | 15 Words
192 Bits | 6 Bits | 198 Bits | 18 Words
224 Bits | 7 Bits | 231 Bits | 21 Words
256 Bits | 8 Bits | 264 Bits | 24 Words
Badge預設值

## Slide 27: BIP 44 – Meaningful structure
m / purpose' / coin_type' / account' / change / address_index
Purpose  固定 44’
Coin type
  Bitcoin  0’
  Eth  60’
Account
Change
  0 for External chain 收款/付款用
  1 for internal chain  內部處裡用
Address index
Badge預設: m/44’/60’/0’/0/0
Tool:https://coinomi.com/recovery-phrase-tool.html

## Slide 28: BIP 44 – Meaningful structure
m / purpose' / coin_type' / account' / change / address_index
Purpose  固定 44’
Coin type
  Bitcoin  0’
  Eth  60’
Account
Change
  0 for External chain
  1 for internal chain
Address index
Badge預設: m/44’/60’/0’/0/0
Tool:https://coinomi.com/recovery-phrase-tool.html
Hardened key

## Slide 29: 乙太幣交易
To Who
  交易對方的Address
  20byte
How much
  金額 單位為wei
  Uint256_t
Gas Price
  手續費 單位為wei
  Uint256_t
Gas Limit
  運算數量
  Uint256_t
Nonce
  交易筆數
Data
RLP encoder
keccak256
Secp256k1
橢圓曲線
Transaction Data
Transaction Hash
Transaction Signature
Recursive Length Prefix
Encoder for variable length binary data

## Slide 30: 乙太幣交易
To Who
  交易對方的Address
  20byte
How much
  金額 單位為wei
  Uint256_t
Gas Price
  手續費 單位為wei
  Uint256_t
Gas Limit
  運算數量
  Uint256_t
Nonce
  交易筆數
Data
Transaction Signature
RLP encoder
Broadcast Transaction data
https://steemit.com/ethereum/@n-ur/behind-the-scene-on-how-myetherwallet-works-simple-illustration

## Slide 31: Smart Contract : Program on ETH
Smart Contract: 類似一種部屬在乙太幣網路的一段程式碼
藉由交易來傳遞/運算資料
一旦交易的對象是Smart Contract，Data會傳遞到對應的程式執行

## Slide 32: ERC20 – define Interface (Application Binary Interface)
TotalSupply
BalanceOf (address _owner)
transfer(address _to, uint256 _value)
transferFrom(address _from, address _to, uint256 _value)
approve(address _spender, uint256 _value)
allowance (address *_owner*, address *_spender*)

## Slide 33: 怎麼交易ERC20?
Contract Address
How much meaning less
Gas Price
Gas Limit
Nonce
Data
對於錢包來說，ERC20只是帶有Data的交易
能夠塞Data就代表能支援ERC20，只是不一定有辦法顯示相對應的交易資料
To Who
How much
Gas Price
Gas Limit
Nonce
Data
Contract Method
Contract Data

## Slide 34: ERC20 Data format
Contract Method – 4 Byte  Hashed Application Binary Interface
Contract Data – Depend on function
EX:
transfer(address _to, uint256 _value)
4 Byte
32 Byte
32 Byte
Data
Detail: https://github.com/ethereum/wiki/wiki/Ethereum-Contract-ABI

## Slide 35: ERC20 Data format
Example: 要轉 1 個 Hitcon Token給我的話
transfer(0x4bf5193805a4fd033b84b5bb700bf2a2aaae6a7d, 0xDE0B6B3A7640000)
“transfer(address,uint256)” SHA3 a9059cbb2ab09eb219583f4a59a5d0623ade346d962bcd4e46b11da047c9049b
Address  Append to 32Bytes
0x0000000000000000000000004bf5193805a4fd033b84b5bb700bf2a2aaae6a7d
Value  Append to 32Bytes 0x000000000000000000000000000000000000000000000000de0b6b3a7640000
Data:0xa9059cbb0000000000000000000000004bf5193805a4fd033b84b5bb700bf2a2aaae6a7d0000000000000000000000000000000000000000000000000de0b6b3a7640000

## Slide 36: Secure Element – Why?
雖然錢包可以透過軟體實作，但是容易造成Master Key被偷
冷錢包，透過一個專門的硬體去存放/使用Master Key
但是即使是冷錢包，實作方式主要分成兩類
  MCU Ex:TREZOR
  Secure Element + MCU Ex:Ledger Wallet

## Slide 37: Secure Element – Why?
TREZOR  透過MCU實作
通常絕大多數的MCU都難以抵抗Side-channel攻擊，所以較為容易被破解
Ex: https://jochen-hoenicke.de/trezor-power-analysis/ P.S 已經Fix了

## Slide 38: Secure Element – Why?
https://jochen-hoenicke.de/trezor-power-analysis/

## Slide 39: Secure Element – Why?
而Secure Element最主要的目的就在於如何防止Side-channel
IC廠商會加上不同的Anti-tampering方法
常見於信用卡/SIM卡等晶片上

## Slide 40: Secure Element - Usage
SPI Driver
Secure Element Driver
Wallet Application
Transaction Application
RLP encoder + keccak256
Init Wallet/Create Account/…
ADPU cmd process
MT7697 SPI Driver
Software SPI Driver

## Slide 41: Secure Element - State
Init
No Host
Disconnect
Normal
Perso
Perso?
Bind Reg
BackToNoHost
-with pin code
Bind Login
BackToInit – with Vender Key
Bind Logout
InitDevInfo

## Slide 42: Host Registration
Host
SE
BindRegInit (UUID, Description, HASH)
Handle, (OTP)
Get UUID of the Host
BindRegChlng (Handle)
Challenge
Calculate devKey from UUID & OTP
Calculate Response of Challenge by devKey
BindRegFinish (Handle, Response)
HostId, Confirm Status
Verify Response
Store Host if Passed

## Slide 43: Host Login
Host
SE
Get UUID and OTP from storage
BindLoginChlng (HostId)
Challenge
Calculate devKey from UUID & OTP
Calculate Response of Challenge by devKey
Bind Login (HostId, Response)
Status Words, 0x9000 if success
Verify Response

## Slide 44: Device Key (devKey) Derivation
UUID of Host
32 bytes
OTP from SE
6 bytes
SHA256
devKey
32 bytes

## Slide 45: Challenge and Response
Response of Host
16 bytes
Challenge from SE
16 bytes
AES256
devKey
32 bytes
ECB mode, Non-Padding

## Slide 46: Encrypt Key and MAC Key
Encryption Key
  Used for Data Encryption after Login
Mac Key
  Used for Data HMAC-SHA256
Device Key
32 bytes
“ENC”
3 bytes
SHA256
Encryption Key
32 bytes
“MAC”
3 bytes
SHA256
Mac Key
32 bytes
https://en.wikipedia.org/wiki/Hash-based_message_authentication_code
Login Challenge
16 bytes
Device Key
32 bytes
Login Challenge
16 bytes

## Slide 47: HDW Management
Secure Element Handles BIP32 Path
  m/BIP44/coin/Account/Change/Address
  Badge預設: m/44'/60'/0'/0/0
Secure Element Holds up to 5 accounts
  External Address Pointer of each account (update to 2128 addresses)
  Internal Address Pointer of each account (update to 2128 addresses)

## Slide 48: Cmd line Management
  QueryAccountKey: Query Public Key for a specific Account/Key_ID
  Usage: QueryAccountKey [account] [key_id]
  CreateAccount: Create a New Account for a specific cointype/account_id
  Usage: CreateAccount [cointype] [account_id] [Name]
  QueryAccountInfo: Query a specific Account Info
  Usage: QueryAccountInfo [account_id]
  CreateNextAddr: Generate a new key for a Specific Account
  Usage: CreateNextAddr [account_id]
Account ID:0~4

## Slide 49: Cmd line Management
  SEState: Query Secure Element State
  BindReg: Bind Register
  BindLogin: Bind Login
  BindLogout: Bind Logout
  BackToNoHost: Back to NoHost state
  BackToInit: Back to Init State
  InitDevInfo: InitDeviceInfo and confirm
  PINAuth: Auth Pin Code
  InitWallet: Initialize Wallet from Mnemonic Words
  QueryWalletInfo: Query Wallet Info
  QueryAllAccount: Query All Account Info
  QueryAccountKey: Query Public Key for a specific Account/Key_ID
  CreateAccount: Create a New Account for a specific cointype/account_id
  QueryAccountInfo: Query a specific Account Info
  CreateNextAddr: Generate a new key for a Specific Account
  Transaction: Generate a new Raw Transaction
  Misc.
  Voltage: Read Battery Voltage
  ReinitBLE: Re-init BLE
  AddVcard: Adding a Vcard
  ResetHitconTokenDisplay: Reset Hitcon Token counter

## Slide 50: Cmd line Usage
USB to UART IC: CP2102N
Driver: Linux & Windows & Mac https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
  Mac OSX 10.11 up: Apple Blocked kernel extension.
  https://stackoverflow.com/questions/47109036/cp2102-device-is-not-listed-in-dev-on-macos-10-13 (Note: Answer 2)
Setting:115200 8N1

## Slide 51: Cmd line Usage

## Slide 52: HDW Management
  Account Purpose: 2C 00 00 00  44
  Account Cointype: 3C 00 00 00  60
  Little endian

## Slide 53: HDW Management
Tool:https://coinomi.com/recovery-phrase-tool.html

## Slide 54: Badge initialize + re-generate wallet
Enter
No-Host State
First time initialize
Bind Register
Enter Discon.
Back To Init & Init
Bind Login, Set Pin Code and enter
Normal State
Generate/
Input
Master Key
Initialize Master Key
Initialize Account
m/44’/60’/0’
Initialize address index 0
Read Public Key of address index 0
User Request for re-generate

## Slide 55: Secure Element - State
Init
No Host
Disconnect
Normal
Perso
Perso?
Bind Reg
BackToNoHost
-with pin code
Bind Login
BackToInit – with Vender Key
Bind Logout
InitDevInfo

## Slide 56: Badge startup wallet
Read Status Reg
Bind Login
Calc ETH Address
Read Public Key of m/44’/60’/0/0/0
0x06
0x07
other
Init Wallet
Read Version
If bootloader mode, jump

## Slide 57
Wallet Address
BLE AES Key
QR-Code
格式:
Hitcon://pair?v=版本數
&a=錢包Address
&k=AES Key
&s=ServiceUUID
&c=Characteristic前四個Byte[6]
初始化的時候，
Badge會將生成好的Public Address和BLE Key打包成一個網址顯示在QR Code上面
BLE 各charastic UUID前4byte
Example:
hitcon://pair?
v=18&
a=808c2257d778e5f1340d9325116f5a7273b33f5d&
k=09626aa096254e8a8ce871bfd7b8895c&
s=1cbfbb33-ffc7-c966-77f9-311c6ba9e425&
c=26ccce12e2c66a0b72c50cca509dbfc1275074f57e7c5668
BLE Service UUID
Hitcon Badge 2018 – BLE Initialize + Re-paring

## Slide 58
為了避免濫發交易訊息，UUID是綁定時隨機產生的
QR Code會寫Characteristic UUID的前4個Byte，後面的UUID與Service相同
QR code的Characteristic順序如下:
Hitcon Badge 2018 – BLE UUIDs
Transaction, Txn, AddERC20, Balance, General Purpose Cmd, General Purpose Data
EX:
[init_BLE] LFLASH_Saved_UUID:
ServiceUUID: 8b15cb6c-0dfd-553a-9302-3cdcded12f56
Transaction_UUID: bbf16eb7-0dfd-553a-9302-3cdcded12f56
Txn_UUID: d754e76e-0dfd-553a-9302-3cdcded12f56
AddERC20_UUID: 448821bb-0dfd-553a-9302-3cdcded12f56
Balance_UUID: 19aceb1f-0dfd-553a-9302-3cdcded12f56
General_CMD_UUID: 8a2c0cd1-0dfd-553a-9302-3cdcded12f56
General_Data_UUID: 4ff47ce6-0dfd-553a-9302-3cdcded12f56

## Slide 59
QR-Code
generate
User Request for Re-paring or
First time config
Reset
Wait for connection
Main Menu
MT7697沒辦法 on-flight 修改BLE，
所以必須Reset一次
Hitcon Badge 2018 – BLE Initialize + Re-paring

## Slide 60
AES encryption + Encoding
Raw Data
AES encryption
16Byte Random IV
Encrypted Data
Encrypted Data
16Byte Random IV
Payload
Append to 128 Byte
Encoding Format:
Header1(uint8_t) length1(uint8_t) Data1[len]
Header2(uint8_t) length2(uint8_t) Data2[len]
Header3(uint8_t) length3(uint8_t) Data3[len]

## Slide 61
Transaction
1.To Address
2.Value
3.Gas Price
4.Gas limit
5.Noice
6.Data
AES encryption + Encode
Write to Transaction Characteristic
Badge notify
Txn Gatt
ERC20的Data帶進去
Badge會Parsing這部分的Data顯示出來

## Slide 62
Update Balance or ERC20 Balance
Value
Write to Balance Characteristic
1.Address
2.Value
Encoding Format:
0x01 0x14 ADDRESS 0x02 0x08 Value(Double)
AES encryption + Encode
Badge 並不會知道Balance是否正確!

## Slide 63: Apple, Why….
6/12 Update
感謝＠CW Cai支援

## Slide 64: Prototypes

## Slide 65: 靈感來源
Hacker Warehouse Electronic Badge
https://hackerwarehouse.com/product/hacker-warehouse-electronic-badge/
https://wiki.sha2017.org/w/Projects:Badge
SHACamp 2017 badge

## Slide 66: Prototypes

## Slide 67: 後記 - Prototypes

## Slide 68: 後記 – 生產線

## Slide 69: 後記 – 生產線

## Slide 70: 後記 – 生產線

## Slide 71: 後記 – 生產線

## Slide 72: 後記 – 生產線

## Slide 73: 後記 – 生產線

## Slide 74: 後記 – 生產線

## Slide 75: 後記 – 生產線- Team Work

## Slide 76: 後記 – 生產線- Team Work

## Slide 77: 後記 – 生產線- Team Work

## Slide 78: 感謝廠商
www.ikv-tech.com
銓安智慧科技
邁特電子
www.might.com.tw

## Slide 79: 資料
Hardware 和 Badge Software 都是 Open-Sourced
Github: https://github.com/will127534/HITCON-Badge-2018/
Android: https://github.com/johnny5581/HitconWalletJava
  Big Thanks to @Nagi @WizTonE @Aaron Luo for the Android App
Hitcon Badge 2018 Arduino Boards support package:
https://raw.githubusercontent.com/will127534/HITCON-Badge-2018/master/Software/Arduino_packages/package_hitcon_badge_index.json
Linkit 7697: https://labs.mediatek.com/zh-tw/chipset/MT7697